## Slide 1: Ⅰ. LiDAR 카메라
D435, D435i
Depth Technology : Active Stereo
L515
Depth Technology : ToF

## Slide 2: Ⅱ. 현 추종 모드 문제점
Issue 1 During the Mobile robot follow User, Obstacleor Person enter into obstacle zone.
Issue 3 During the Mobile robot follow User, Tracked Person is out of Tracking Range.
Issue 2 During the Mobile robot follow User, Tracked Person is close to wall.

## Slide 3: Ⅱ. 현 추종 모드 문제점
Issue 3 During the Mobile robot follow User, Tracked Person is out of Tracking Range.
if (skip_detection > 10) {
mc->clearVelocity();
mc->publishVelocity();
run =3;
}
Because there is no delay function, skip detection is fast increase.
userArrayCallback(const mpc_follow_mode::TrackerUserArrayConstPtr &ptr)

## Slide 4: Ⅱ. 현 추종 모드 문제점
Issue 1 During the Mobile robot follow User, Obstacle or Person enter into obstacle zone.
if ((scanner_z != 0.0 && scanner_z < OBSTACLE_MAX_Z) || (point_z != 0.0 && point_z < OBSTACLE_MAX_Z)
) {
if(detect == 1){
near_user = true;
mc->clearVelocity();
mc->publishVelocity();
run = 3;
}
}
else
{
if (run == 1 && detect == 1)
{
run = 3;
near_user = true;
mc->clearVelocity();
mc->publishVelocity();
}
}
obstacleCallback(const mpc_follow_mode::ObstacleConstPtr &ptr)

## Slide 5: Ⅲ. 현 추종 모드 동작 과정
Laser Scanner Data scan
인식요청
Object distance area
Morphology 연산
Labeling
작업자 인식 여부
Object 인식 여부
추적 객체 중심 Object 제거
추적 객체 중심 Scan 영역 제한
Object Publish
N
N
Y
Y
N
Intersection over Union
Predict location & correction using Kalman Filter
Tracking Person
작업자 추적 여부
작업자 위치 추정
Y
Calculation linear & angular speed
Adaptive Speed Control
Constant Speed Control
Move Control
Person recognition
Person tracking
Move control

## Slide 6: Ⅲ. 현 추종 모드 동작 과정
min_y
max_y
c_y
max_x
c_x
min_x
limitDetectArea();
removeObject();
detectMorpology();
detectCreatelabel();
detectCalculationDistace();
Polar() -> Cartesian();
scanCallback(const sensor_msgs::LaserScan::ConstPtr& scan);
Obstacle_Zone & Tracker Zone
overlapping_area();
userArrayCallback(const mpc_follow_mode::TrackerUserArrrayConstPtr &ptr);
intersection_over_union();
predict_kalman_filter();
Union area = current_area + predict_area – overlapping_area
union area
overlapping area
iou =

## Slide 7: Ⅲ. 현 추종 모드 동작 과정
x
y
mc->moveScanner(trackerUser.tracker_id, frame_id, trackerUser.center_of_mass);
MoveControl::moveScanner(int userId, std:;string scanner, ::geometry_msgs::Vector3 scanner_object);
scannerCalculateVelocity(userId, scanner, scanner_object);
MIN_DISTANCE
MAX_DISTANCE
Follow Mode
Drive Mode
PERSON_NEAR
PERSON_IN_ZONE
PERSON_FAR
gain_p
gain_d
gain_p_angle
gain_d_angle
cmd->linear.x
cmd->angular.z
publishVelocity();
PERSON_NEAR
PERSON_IN_ZONE
PERSON_FAR
Distance : scanner_object.y
Direction : err_p_angle, err_d_angle
Point3D userCoordinate.getAngleFromOrigin() * (3.14159 / 180)

## Slide 8: Ⅳ. LiDAR 카메라 연동 방안
Target Detection
Motion Control
(Sensor Data Fusing)
LRF
Camera
Wheel
Network
SPEAR-MX8
Image data
Jetson Nano
Command
Detection data
Vision & LRF based Tracking System Configuration
LRF
Camera
Environment State
Sensor Fusion
Tracking Info
Direction : θc
Distance : Dc
Direction : θl
Distance : Dl
Camera Weight : Cw
LRF Weight : Lw
Tracking Direction : θ
Tracking Distance : D
Environmental Adaptive Sensor Fusion Model

## Slide 9: Ⅳ. LiDAR 카메라 연동 방안
Person detection
cv::CascadeClassifier
load(const String &filename)
detectMultiScale(InputArray image, std::vector<Rect> &objects, std::vector<int> &numDetections,
double scaleFactor = 1.1, int minNeighbors = 3, int flags = 0, Size minSize = Size(),
Size maxSize = Size())
Point(x1, y1)
Point(x2, y2)
detectMultiScale()
rectangle()
Input image
Return detected Object Rectangle Point
Draw Rectangle based Point in input image
HAAR
HOG(Histogram of Oriented Gradients)
YOLO(You Only Look Once)
SSD(Single Shot Multibox Detector)
Detection Algorithms

## Slide 10: Ⅳ. LiDAR 카메라 연동 방안
Input Image
Person Detect
Framework : TensorFlow
Require DC 5V 4A Power Adapter to execute heavy program. (YOLO)
CNN Model : SSD Mobilenet –V2
FPS : ?
mAP : ?
OpenCV 4.1.1
JetPack 4.2.2
L4T

## Slide 11: Ⅳ. LiDAR 카메라 연동 방안
RGB Image
Tracking Person Info
Person detection
Calculate detection Coordinate
Measure Distance
Command Velocity (Linear & Angular)
Person detection : If frame is increased, very slow fps. So, Video Frame is recommended Size(200, 200) to run similarly to real-time.
 | Y | N
fps | 1 ~ 2 fps | 10 ~ 19 fps
Above the table shows the number fps which uses the detectMultiScale function. The Frame Size if 640 x 480 pixel.
To Increase FPS,
1. PC Spec UP
2. Change Detection Function Parameter
3. Change Detection Algorithm

## Slide 12
class DisplayFollowInfo()
{
void display_start_info();
void display_stop_info();
void display_follow_drive_info(int cmd, int detect_user, int detect_obstacle);
void display_skip_detection();
void display_clear();
}
void display_start_info();

## Slide 13
class DisplayFollowInfo()
{
void display_start_info();
void display_stop_info();
void display_follow_drive_info(int cmd, int detect_user, int detect_obstacle);
void display_skip_detection();
void display_clear();
}
void display_follow_drive_info(cmd, detect_user, detect_obstacle);
void display_skip_detection();
void display_stop_info();

## Slide 14: Ⅱ. 현 추종 모드 문제점 해결 전략
Boundary Box
Issue 1
Issue 2
Issue 3
Solution 1
Solution 2
Solution 3
Detection Zone
Detection (Method 2)
Make Tracker initial box
Update Tracking box (GOTURN)
Extract tracker_id, position Info
Total Frame

## Slide 15: Ⅱ. 현 추종 모드 문제점 해결 전략
Total Frame
Detection Zone
Detection Zone
Detection Zone
Tracker | Speed | Accuracy | Redetection
Boosting | Low | Low | X
MIL |  |  | X
KCF | Low | High | O
TLD |  |  | X
MEDIANFLOW |  |  | X
GOTURN | Normal | High | O
MOSSE | Fast | Low | X
CSTR | Low | High | X
Method 1
Method 2
Tracker::init(frame, box)
Tracker::update(frame, box)

## Slide 16: Ⅱ. 현 추종 모드 문제점 해결 전략
Method 2
Rectengle (width / 2, height / 2)
Average N-Point Position value
Method 1
Intersection Position value
Original Method

## Slide 17: Ⅱ. 현 추종 모드 문제점 해결 전략
Issue 1
Solution 1
Distance_C
Distance_L

## Slide 18: Ⅱ. 현 추종 모드 문제점 해결 전략
Issue 2
Solution 2
?

## Slide 19: Ⅱ. 현 추종 모드 문제점 해결 전략
Issue 3
Solution 3
Tracking Person Missing?
Stop
Skip_detection ++
Not Yet Detection?
Increase Detection Range
Following Person
Not Yet Detection?
Restart